## Slide 1: Spin echo Pulse sequence Spin echo principle
V.G.Wimalasena
Principal
School of Radiography

## Slide 2: Introduction
This is the basic pulse sequence in MRI
It is designed to obtain a high MR signal by converting the decay signal to a growing signal (an echo of the decay signal)
It uses , first, 900 RF pulse and then a 1800 RF pulse before obtaining the MR signal

## Slide 3: Basic data collection procedure
Slice selection
    Gradient selection
    RF band width selection
Pulse sequence selection
Phase encoding selection
    Done by appropriate gradient selection
Frequency encoding selection
    Done by appropriate gradient selection
Application & data collection

## Slide 4: Demonstration of Frequency Encoding & Phase Encoding
Number of Pulse repetitions (TR steps) is decided by the number of phase encoding steps of the rows in the matrix

## Slide 5: The need of 1800 RF pulse
To repahse the dephasing nuclei to get more data samples from the MR signal
Fast
Fast
Slow
Slow
Nuclei dephasing after removal of 90 pulse
Inversion by 180 pulse
Nuclei rephasing after inversion

## Slide 6: Result of 1800 pulse

## Slide 7: The spin echo pulse sequence
A pulse sequence that uses a 900 excitation pulse first and then a 1800 RF pulse to convert dephasing nuclei to rephasing nuclei is called a spin echo pulse sequence.
Dephasing caused by magnetic field inhomogeneities also is compensated by the 1800 RF pulse.
90
180
Echo

## Slide 8: Spin echo procedure
It starts with a 900 excitation pulse to flip the NMV into the transverse plane.
The NMV precesses in the transverse plane and T2 decay starts.
In addition to that due to the presence of magnetic field inhomogenities it increases the decay rate so T2* dephasing occurs.

## Slide 9
The T2* dephasing causes the magnetic moments to dephase or ‘fan out’ in the transverse plane.
The magnetic moments are now out of phase with each other, i.e. they are at different positions on the precessional path at any given time.
The magnetic moments that slow down, form the trailing edge of the fan, and the magnetic moments that speed up, form the leading edge of the fan
A 1800 RF pulse is then used to compensate for the dephasing
The 1800 RF pulse has sufficient energy to move the NMV through 1800

## Slide 10
The 1800 RF pulse flips these individual magnetic moments through 1800.
They are still in the transverse plane, but now the magnetic moments that formed the trailing edge before the 1800 pulse, form the leading edge.
Conversely, the magnetic moments that formed the leading edge prior to the 1800 pulse, now form the trailing edge.
The direction of prescession remains the same, and so the trailing edge begins to catch up with the leading edge.

## Slide 11
At a specific time later, the two edges are superimposed.
The magnetic moments are now momentarily in phase because they are momentarily at the same place on the precessional path.
At this instant, there is transverse magnetization in phase , this is called a spin echo
So a high signal is induced in the coil at this moment.
In practice the signal is detected and sampled during rephasing and the dephasing that follows.
The spin echo signal now can be used to get T1 and T2 information as T2* dephasing has been reduced.

## Slide 12: Spin Echo - RF Rephasing
B0
B0
B0
B0
B0
B0
900 RF
1800 RF is applied before complete dephasing occurs
T2* dephasing
rephasing
F
S
S
F
Result if allowed to dephase

## Slide 13: Spin Echo - RF Rephasing
B0
B0
B0
B0
B0
B0
900 RF
1800 RF is applied before complete dephasing occurs
T2* dephasing
rephasing
F
S
S
F
S
F
Result if allowed to dephase
Result in high NMV flipped by 1800

## Slide 14
http://mriquestions.com/uploads/3/4/5/7/34572113/1517606_orig.gif

## Slide 15: Timing parameters in spin echo
TR is the time between each 900 excitation pulse.
TE is the time between the 900 excitation pulse and the peak of the spin echo.
The time taken to rephase after the application of 1800 RF pulse, equals the time the NMV took to dephase when 900 RF pulse was withdrawn.
This time is called the (ζ)Tau time
The TE is therefore twice the Tau time.
  TE = 2 ζ

## Slide 16: Spin echo pulse sequence
900 RF pulse
1800 RF pulse
Spin echo
ζ (Tau)
ζ (Tau)
TE
TE = 2 ζ

## Slide 17: Spin Echo

## Slide 18: Multiple echoes
After sampling the signal another 180 pulse can be applied to rephase the NMV and can obtain another signal
So more than one 1800 RF pulse can be applied after the 900 excitation pulse.
Each 1800 pulse generates a separate spin echo that can be received by the coil and used to create an image.
One, two or four 1800 RF pulses can be used in spin echo, to produce one , two or four different images.

## Slide 19: Using one echo (T1 weighting)
The pulse sequence can be used to produce T1 weighted images if a short TR and TE are used.
One 1800 RF pulse is applied after the 900 excitation pulse.
Short TE ensures that only a little T2 decay has occurred, and, the differences in the T2 times of the tissues do not dominate the echo and its contrast.
Short TR ensures that fat and water vectors have not fully recovered , so the differences in their T1 times dominate the echo and its contrast.

## Slide 20: Spin echo T1 weighting
900 RF pulse
1800 RF pulse
Single Spin echo
TAU
TAU
Short TE
Short TR
900 RF pulse

## Slide 21: Multi-echo Spin Echo
As long as T2-relaxation has not completely destroyed the MR signal, it is possible to stimulate the system with additional 180°-pulse(s) and generate additional echo(es).
But the amplitude of each echo is progressively smaller due to T2 decay.

## Slide 22: Spin echo using two echoes ( T2 weighting & Proton density )
The first spin echo is generated early by selecting a short TE. (Only a little T2 decay has occurred and so T2 differences between tissues are minimal in this echo)
The second spin echo is generated much later by selecting a long TE
A significant amount of T2 decay has now occurred, and so the differences in the T2 times of the tissues are maximized in this echo.
The TR selected is long , so that T1 differences between tissues are minimized.
The first spin echo therefore has a short TE and a long TR and is proton density weighted.
The second spin echo has a long TE and a long TR and is T2 weighted.

## Slide 23: Dual echo - T2 weighting & Proton density
Long TR
1st TE (short)
2nd TE (long)
1st spin echo proton density
2nd spin echo T2
900
900
1800
1800

## Slide 24: Dual-eco Spin echo

## Slide 25
A few decades ago Dual-echo SE sequences like the one pictured above were a standard technique.
The first echo (at short TE) provided "spin-density" contrast while the second echo (at long TE) provided T2-weighted contrast.
Today, T2-FLAIR has largely supplanted spin-density-weighted SE images for most applications, so multi-echo SE is only occasionally used.

## Slide 26: Fast (Turbo) Spin Echo (FSE)
Multi-echo SE should be distinguished from FSE where multiple 180°-pulses and echoes also follow each 90°-pulse.
The simplified FSE pulse-echo timing diagram appears below

## Slide 27
Superficially this appears similar to multi-echo SE, although you may note that the echoes are not uniformly diminishing in size with increasing TE multi-echo SE as expected.
The reason the echoes look different is because in FSE different phase-encoding gradients (not shown) are being applied with each 180°-pulse.
In single echo and multi-echo SE imaging, the phase-encoding gradient is turned on only once in each TR interval. Depending on the number of echoes, in FSE imaging the phase-encoding may be applied 8, 16, 32 or more times in each TR interval.

## Slide 28: Summary
A spin echo pulse sequence uses a 900 excitation pulse followed by one or more 1800 rephasing pulses to generate one or more spin echoes.
Spin echo pulse sequences produce either T1, T2 or proton density weighting.
TR controls the T1 weighting.
  Short TR maximizes T1 weighting
  Long TR maximizes proton density weighting
TE controls the T2 weighting
  Short TE minimizes T2 weighting
  Long TE maximizes T2 weighting

## Slide 29: Next
Gradient echo pulse sequence